## Slide 1
P0
P1
P2
P3
P4
P5
P6
P7
P8
PB15
PB14
PB13
PB12
PB10
PB11
PA5
PD12
PD13
3.3V Rail (250 mA supply Max)
GND Rail
Not Connected
ADC
DAC
UART 3
TX
UART 3
RX
SPI 2
SCLK
SPI 2
MISO
SPI 2
MOSI
SPI 2
SS
I2C 2
SDA
I2C 2
SCL
Servo 1
Servo 2
OpenMV Cam
LED1 – Red
LED2 – Green
LED3 – Blue
LED4 – IR
Micro SD Slot
SD < 2GB Max
SDHC < 32GB Max
SDXC < 2TB Max
Pin
Name
CPU
Name
Pin
Name
CPU
Name
Frame Sync (use to frame sync cams)
BOOT 0 (Connect to 3.3V for DFU mode)
Reset (Connect to GND to reset)
TIM4 CH1
TIM4 CH2
Peripherals / Timers
Peripherals / Timers
All pins are 5V tolerant1 with a 3.3V output
All pins can sink or source up to 25 mA2
1 P6 is not 5V tolerant in ADC or DAC mode
2 Up to 120mA in total between all pins
Max current used wo/ µSD card < 150 mA
Max current used w/ µSD card < 250 mA
By: Ibrahim Abdelkader & Kwabena W. Agyeman
https://openmv.io
CAN2 RX
CAN2 TX
P9
PG3
I2C4
SDA
I2C4
SCL
UART 1 RX
UART 1 TX